## Slide 1: Hazardous Materials Awareness
2023
Notes: Hazardous Materials Awareness Training 2020-2021
  Course Length
    1.0 Hour

## Slide 2: Hazardous Materials Awareness Level
  OSHA 1910.120(g)(6)(i)
    First responders at the awareness level are individuals who are likely to witness or discover a hazardous substance release and who have been trained to initiate an emergency response sequence by notifying the proper authorities of the release. They would take no further action beyond notifying the authorities of the release.
Notes: Notes for the Instructor:
  Read OSHA description of Haz. Mat. Awareness level responder
  Discuss this description to the class and discuss who this encompasses:
    Fire
    EMS
    Law Enforcement
    Public Works
    DOT

## Slide 3: Training Objectives (1 of 2)
The responder shall understand what hazardous substances are and the risks associated with them in an incident.
Notes: Notes for the Instructor:
  Review briefly and move on.

## Slide 4: Training Objectives (2 of 2)
The responder shall understand their role in the emergency response including site security and control and the use of the U.S. D.O.T Emergency Response Guidebook.
The responder shall have the ability to realize the need for additional resources, and to make the appropriate notifications to the communication center.
Notes: Notes for the Instructor:
  Review briefly and move on.

## Slide 5: Hazardous Substances
Dangerous goods, also called hazardous materials or Haz. Mat., are solids, liquids, or gases that can harm people, other living organisms
Notes: Notes for the Instructor:
  This is the OSHA definition of hazardous substances.
  As a group, discuss examples of Haz. Mat.

## Slide 6: Dangers of Hazardous Substances
Contamination
Illness
Injury
Death
Long Lasting Environmental Effects
Decomposition
Chemical Degloving from Sulfuric Acid Exposure
Notes: Notes for the Instructor:
  Read each danger type to group and discuss examples of each:
    Contamination – Discuss contamination with group and discuss ideas of the concept.
    Illness – Humans, plants, animals.
    Injury – People, plants, planet
    Death – Acute and long term effects
    Long lasting environmental effects – 10 / 20 / 50 / 100 year problems
    Decomposition – Rapid eating away at solids.

## Slide 7: Haz. Mat. Identification
Visual Cues
NFPA 704
Placards
SDS
Shipping Papers
Notes: Notes for the Instructor:
  As a group, discuss the visual cues and give examples:
    Visual Cues:
      Vapor Clouds
      Visible Fluids
      Containers
    The 4 other identifying systems are covered in the next several slides

## Slide 8: NFPA 704
(OXY – Oxidizer / ACID – Acid / ALK – Alkali / COR – Corrosive)
Notes: Notes for the Instructor:
  Explain each section of the NFPA 704 diamond
    Blue – Health (0 – 4)
    Red – Flammability ( 0 – 4 )
    Yellow - Reactivity (0 – 4)
    White – Special Hazards
  Discuss where the 704 system is used and how it is beneficial to first responders

## Slide 9: ERG and Shipping Papers
The 2020 ERG has a special section (inside the front cover) that specifically covers shipping papers.
Notes: Notes for the Instructor:
  This slide is an introduction slide.
  Have students open the 2020 ERG to the inside front cover
  Go to the next slide

## Slide 10: Emergency Response Guidebook
Use during initial phase of incident
5 Sections
  Yellow
  Blue
  Orange
  Green
  White
Notes: Notes for the Instructor:
  Discuss when the ERG is used doing an emergency
    Highlight that the ERG is an INITIAL reference for first responders, not the ONLY reference
    Changes of the 2020 ERG are discussed next
    Each color section is detailed after

## Slide 11: Summary of changes to the 2020 ERG
Link to 2020 ERG Changes

## Slide 12: The White Section
Shipping Papers
A “Down and Dirty” How To guide
Emergency Response Steps
Introduction to using the Placards Table
Notes: Notes for the Instructor:
  The front white pages:
    Response information instead of instructions to use.
    Added Information
    Inside front cover is the shipping papers document
    Page 1 is a brief “How To” for anyone who has never used the ERG, not a detailed instruction manual.
    An introduction to the Page 7 Placards table has been added.

## Slide 13: White Reference Section
The “White” Pages
  The instructions
  Size Up information
  Definitions
  BLEVE Table ( Page 367)
  CBRNE Information (Page 368)
  Contact Information (Page 391)
Notes: Notes for the Instructor:
  The rear White section is a collection of usual information that is not normally referenced during an emergency situation
  Page 354 thru 359 – The instructions on how to use the book
  Page 365 is the BLEVE information section
    Page 367 is the BLEVE distances and fire flow table
  Page 368 is a CBRNE reference Guide
    THIS SECTION IS A REFERENCE FOR EDUCATION AND SHOULD NOT BE A GUIDE USED DURING AN CBRNE EMERGENCY
    Page 373 is an IED stand off distance guide
      Brief table of probable safe distances dealing with IED
  Glossary on pages 375 – 385
  Contact information Page 391

## Slide 14: Placards
Notes: Notes for the Instructor:
  Have the students go to pages 8-9 in the 2012 ERG
  Each hazard class has its own group of placards
    Discuss the 9 hazard classes and the placards color and description that are within that hazard class
      Hazard class 1 – Explosives
      Hazard class 2 – Poisonous Gases
      Hazard class 3 – Compressed Gases
      Hazard class 4 – Flammable Solids
      Hazard class 5 – Oxidizers
      Hazard class 6 – Poison Liquids
      Hazard class 7 – Radioactive substances
      Hazard class 8 – Corrosives
      Hazard class 9 – Misc. Haz. Mat

## Slide 15: Placards Table
Notes: Notes for the Instructor:
  Have all students go to page 8-9
  Note that a new placard has been added under guide 111 “Misc. Cargo” placards in the upper left hand corner of page 8
    The Y and blank black and white placards are now used for Limited Quantities of Miscellaneous dangerous goods

## Slide 16: Tanks and Trailers Table
Notes: Notes for the Instructor:
  Have users go to page 10-14 and discuss the different tanks, trailers and containers
  Remind students that pages 10-14 are to be used as a LAST resort

## Slide 17: Global Harmonized System (Added in 2016) Pages 16-17
Notes: Discus GHS Pictograms

## Slide 18: Intermodal Container Labeling
Pages 18 – 21 are dedicated to Intermodal Containers
Intermodal container use for hazardous materials transportation was up 42% from 2006 to 2011
Notes: Notes for the Instructor:
  Have users go to page 18.
  Discuss “what are intermodal containers?”
  Discuss how the identification system works
  Discuss the “doubling” of hazards
  Discuss “X” means water reactive
  Have students review pages 18 – 21

## Slide 19: Pipeline Transportation
Pages 22 – 27 are dedicated to Pipeline based emergency response and identification.
Notes: Notes for the Instructor:
  Have group go to page 22.
  Pages 22 – 27 cover Pipeline transportation
  This section has been expanded significantly and you should spend some time discussing this section
  Highlights to cover:
    Structures
      Compressor Buildings / Valves / Meter Stations / Patrol Markers
    Markers
      “Warning” “Caution” “Danger”
      Found at Road, railroad and water crossings
    Natural Gas incidents safety:
      Never extinguish a natural gas fire (Page 25)
      Never operate pipeline valve (Page 25)
    Liquid Pipelines
      Structures
        Storage tanks / Valves / Pump Stations / Patrol Markers
      Markers:
        Found at road, railroad and water crossings

## Slide 20: Yellow Bordered Pages
YELLOW Section is Listed in order of UN number
GREEN Highlights = If no fire, go to GREEN section
Notes: Notes for the Instructor:
  Instruct the class to go to page 28
  The Yellow section is used to find hazardous materials by their UN number
  The Haz. Mat. Highlighted in green identifies that material as being listed in table 1 of the green section.
    Table 1 is initial isolation distances
    ONLY USE THE GREEN SECTION IF THERE IS NO FIRE
  Ask the class “On Page 29 UN Number 1010, the guide number is 116P. What does the P signify?
    (answer is on page 1 of the ERG ---- “P” means material will undergo violent polymerization if subjected to heat or contamination)

## Slide 21: Blue Bordered Pages
BLUE Section is Listed in alphabetical order of the chemical name
GREEN Highlights = If no fire, go to GREEN section
Notes: Notes for the Instructor:
  Instruct the class to go to page 92
  The Blue section is used to find hazardous materials by name
  The Blue section is listed in alphabetical order
  The Haz. Mat. Highlighted in green identifies that material as being listed in table 1 of the green section.
    Table 1 is initial isolation distances
    ONLY USE THE GREEN SECTION IF THERE IS NO FIRE

## Slide 22: Orange Bordered Pages
These are a 2 page section
These sections are designed for ease of use
Guide 111
Notes: Notes for the Instructor:
  Instruct the students to go to page 156.
  The ORANGE guides are set up as a 2 Page Reference section
  The left side is broken down into two parts:
    Potential Hazards and Public Safety
      Potential Hazards is broken into Fire and Health categories
        The higher risk category is always listed first
          Example: Guide 112 Fire is listed first / Guide 120 Health is listed first
      Public Safety
        Protective Clothing Recommendations FOR FIRST RESPONDERS ONLY
        Evacuation Guide
  The right side is the Emergency Response Recommendations:
    Fire Actions
    Spill Actions
    First Aid Actions
GUIDE 111 IS FOR USE ONLY WHEN THERE IS ABSOLUTELY NO OTHER WAY TO DETERMINE THE CHEMICALS INVOLVED

## Slide 23: Green Bordered Pages
Distance references
Table 1 – Initial Isolation and Protection.
Table 2 – Water Reactive Materials.
Table 3 – Isolation of TIH Gases.(toxic inhalation hazards)
Notes: Notes for the Instructor:
  Instruct the class to go to page 286.
    Page 286 is the introduction the green section
    The Green section contains 3 tables
    Table 1 – Page 294
      Table used to find initial isolation distances as referenced in the yellow and blue sections
      Only used if there is no fire
      Small spills are less than 55 gallons. Large spills are greater than 55 gallons
      NOTE WIND DIRECTION
    Table 2 - Page 344
      Table 2 Is a list of all water reactive materials identified in this book
      These chemicals produce large amounts of Toxic Inhalation Hazard (TIH) gases when mixed with Water
      Table 2 is used when a chemical in table 1 has “WHEN SPILLED IN WATER” following its name
    Table 3 - Page 350
      Table 3 lists the TIH for the six most common TIH gases (Ammonia, Chlorine, Ethylene Oxide, Hydrogen Chloride, Hydrogen Fluoride and Sulfur Dioxide)

## Slide 24: Payroll / Credit
Upon completion of the course and testing please enter payroll / credit time into the Emergency Reporting system.
Please enter this info under the unassigned station field at the bottom portion of the daily roster (add person).
Fill in your name as per usual and then the times select the following for the position and activity codes:
Position : Training
Activity :
  CO -Credit Only (on duty)
  TRN- Training Pay (off duty)
  Type mandatories in the note field.

## Slide 25: THE EXAM
Access Code: HAZCOM